## Slide 1: Data Integrity (For Working-Level Personnel)
GMP Expert Committee, Quality and Technology Committee, Japan Pharmaceutical Manufacturers Association
DI Project - Prepared in May 2019

## Slide 2: Table of Contents (Content for Working-Level Personnel)
Data Integrity - Why must we comply with this? –
What is ALCOA +?
Recommended practices / inadvisable practices
Examples of DI-related deviations (from FDA warning letter)
(Appendix) Glossary (from PIC/S DI guidance 13. Definitions)

## Slide 3: Table of Contents (Content for Working-Level Personnel)
Data Integrity - Why must we comply with this? –
What is ALCOA +?
Recommended practices / inadvisable practices
Examples of DI-related deviations (from FDA warning letter)
(Appendix) Glossary (from PIC/S DI guidance 13. Definitions)

## Slide 4: What is ALCOA+?
Basic principles of data integrity, applicable to both paper and electronic systems.
ALCOA is an acronym that stands for the following.
ALCOA + includes the following
in addition to ALCOA.
A: Attributable L: Legible C: Contemporaneous O: Original A: Accurate
C: Complete C: Consistent E: Enduring A: Available
Chart: 
| Attributable | Legible | Contemporaneous | Original | Accurate | Complete | Consistent | Enduring | Available
Column 1 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111
A
L
C
O
A
+

## Slide 5: A: Attributable
It should be possible to identify the individual who performed the recorded task. The need to document who performed the task / function, is in part to demonstrate that the function was performed by trained and qualified personnel. This applies to changes made to records as well: corrections, deletions, changes, etc.
Chart: 
| Attributable | Legible | Contemporaneous | Original | Accurate | Complete | Consistent | Enduring | Available
Column 1 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111
A
L
C
O
A
+
Make it possible to trace the date and author (or originator).
Create records that ensure the traceability of the work performed.
Use registered signatures and seals for records.

## Slide 6: L: Legible
All records must be legible – the information must be readable in order for it to be of any use. This applies to all information that would be required to be considered Complete, including all original records or entries. Where the ‘dynamic’ nature of electronic data (the ability to search, query, trend, etc) is important to the content and meaning of the record, the ability to interact with the data using a suitable application is important to the ‘availability’ of the record.
Chart: 
| Attributable | Legible | Contemporaneous | Original | Accurate | Complete | Consistent | Enduring | Available
Column 1 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111
A
L
C
O
A
+
Make records legibly and accurately.
Make records that can be understood correctly and easily.

## Slide 7: C: Contemporaneous
The evidence of actions, events or decisions should be recorded as they take place. This documentation should serve as an accurate attestation of what was done, or what was decided and why, i.e. what influenced the decision at that time.
Make records at the same time the operation is performed.
Chart: 
| Attributable | Legible | Contemporaneous | Original | Accurate | Complete | Consistent | Enduring | Available
Column 1 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111
A
L
C
O
A
+

## Slide 8: O: Original
The original record can be described as the first-capture of information, whether recorded on paper (static) or electronically (usually dynamic, depending on the complexity of the system). Information that is originally captured in a dynamic state should remain available in that state.
Do not enter results of implementation in record forms other than hose officially approved.
Do not use sticky notes or memo paper as part of records.
Do not use personal notebooks for recording data or making calculations.
Chart: 
| Attributable | Legible | Contemporaneous | Original | Accurate | Complete | Consistent | Enduring | Available
Column 1 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111
A
L
C
O
A
+

## Slide 9: A: Accurate
Ensuring results and records are accurate is achieved through many elements of a robust Pharmaceutical Quality Management System. This can be comprised of:
equipment-related factors such as qualification, calibration, maintenance and computer validation.
Chart: 
| Attributable | Legible | Contemporaneous | Original | Accurate | Complete | Consistent | Enduring | Available
Column 1 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111
A
L
C
O
A
+
policies and procedures to control actions and behaviours, including data review procedures to verify adherence to procedural requirements
deviation management including root cause analysis, impact assessments and CAPA
trained and qualified personnel who understand the importance of following established procedures and documenting their actions and decisions.

## Slide 10: A: Accurate (continued)
Together, these elements aim to ensure the accuracy of information, including scientific data, that is used to make critical decisions about the quality of products.
Chart: 
| Attributable | Legible | Contemporaneous | Original | Accurate | Complete | Consistent | Enduring | Available
Column 1 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111
A
L
C
O
A
+
Prepare the written procedures, perform the operations in accordance with these, and make records.
Strictly reject dishonest practices related to documents and records (falsification, tampering, etc.)

## Slide 11: C: Complete
All information that would be critical to recreating an event is important when trying to understand the event. The level of detail required for an information set to be considered complete would depend on the criticality of the information. A complete record of data generated electronically includes relevant metadata.
Chart: 
| Attributable | Legible | Contemporaneous | Original | Accurate | Complete | Consistent | Enduring | Available
Column 1 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111
A
L
C
O
A
+
When electronic records are integrated from a computerized system to another system (i.e., when records are not maintained in the original system), transfer or archive meta data (including audit trails and electronic signatures) with the electronic records.

## Slide 12: C: Consistent
Good Documentation Practices should be applied throughout any process, without exception, including deviations that may occur during the process. This includes capturing all changes made to data.
Chart: 
| Attributable | Legible | Contemporaneous | Original | Accurate | Complete | Consistent | Enduring | Available
Column 1 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111
A
L
C
O
A
+
Apply good data management practice to all GMP documents and records. Records include electronic records and electronic signatures.

## Slide 13: E: Enduring
Part of ensuring records are available is making sure they exist for the entire period during which they might be needed. This means they need to remain intact and accessible as an indelible/durable record.
Chart: 
| Attributable | Legible | Contemporaneous | Original | Accurate | Complete | Consistent | Enduring | Available
Column 1 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111
A
L
C
O
A
+
Make paper records in permanent ink.
Store electronic records by secure and validated processes.
Hold documents intact for the duration of the retention period, based on the lifecycle of such documents.

## Slide 14: A: Available
Records must be available for review at any time during the required retention period, accessible in a readable format to all applicable personnel who are responsible for their review whether for routine release decisions, investigations, trending, annual reports, audits or inspections.
Chart: 
| Attributable | Legible | Contemporaneous | Original | Accurate | Complete | Consistent | Enduring | Available
Column 1 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111 | 0.11111
A
L
C
O
A
+
Store batch records and other records supporting the batch quality in a secure and reliable manner so as to be retrievable within a specified period of time and to allow for complete reconstruction of batch history. If a computerized system is used, this should be guaranteed at the time of system update.

## Slide 15: Table of Contents (Content for Working-Level Personnel)
Data Integrity - Why must we comply with this? –
What is ALCOA +?
Recommended practices / inadvisable practices
Examples of DI-related deviations (from FDA warning letter)
(Appendix) Glossary (from PIC/S DI guidance 13. Definitions)

## Slide 16: Key points of data integrity, specific to paper systems (1)
• Procedures outlining good documentation practices and arrangements for document control should be available within the QMS.
Generation , distribution and control of templates used to record data
- Control procedures for written operating procedures and paper record sheets, etc.
Procedures are not specified for the generation, distribution and control of original paper record template.
• Records may be falsified if templates are not controlled!
• An obsolete version of record template may be used if versions and issuance of templates are not controlled!
• Can the contemporaneousness of records be guaranteed if data are recorded on a template other than the one specified?
Recommended practices
Inadvisable practices
Notes: < Recommended actions >
(Concrete contents to be entered in the SOP)
- Issuance control of record templates
• Issue a series of numbered templates as necessary, and check (reconcile) the quantity of all such templates at the time of use.
• Templates that have not been completed or contain errors should be retained as part of a permanent storage record with a statement that these should be replaced.
- Precautions at the time of template generation
• Provide sufficient space for data entry.
• Make a template allowing all critical data to be recorded.
• The design of the paper record template should be such that data can be recorded in the order of the work process and related procedures, so as to reduce the risk of inadvertent deletion of critical data.
- Precautions at the time of generating data/records
• Handwritten entries should be clear and legible.
• Complete any records on operations in a contemporaneous manner.
• Records must be indelible (use ballpoint pen, etc.).
• Sign and date records using a unique identifier to indicate the individual who made the record.
• Corrections to records should be made in a manner that ensures full traceability.
- Retention and control of documents
• Retain SOPs and record templates in a manner that allows for appropriate control of the version number.
• Documents should be appropriately controlled to prevent unauthorized changes, use of obsolete documents and/or draft documents, and loss of master documents.
• If necessary, take measures to prevent records from being soiled (by getting wet or being stained by materials, etc.).

## Slide 17: Key points of data integrity, specific to paper systems (2)
• Procedures outlining good documentation practices and arrangements for document control should be available within the QMS (Continued)
- How completed documents are routinely reviewed for accuracy,
authenticity and completeness;
- Storage method for records
No method for reviewing and controlling various records is not specified. (Continued)
• Incorrect data may be accepted by QA owing to improper review of records!
• It may become impossible to confirm the traceability of paper records printed out directly from the electronic system (e.g., balance, pH meter)!
• Can the integrity of various stored records be guaranteed?
Recommended practices
Inadvisable practices
Notes: < Recommended actions >
- Method of reviewing records
• Records of critical process steps should be reviewed by the following procedure.
[1] A person in charge designated before the start of operation (e.g., production supervisor) should witness the operations and review the records.
[2] An authorized person from the manufacturing unit should review the records before these are sent to QA.
[3] QA (authorized person) should review and approve the records before the manufactured batch is released/shipped.
• At the end of the tests, laboratory records for such tests should be evaluated by the designated personnel (e.g., a second analyst) with checking of all entries and critical calculations in accordance with the principles of data integrity.
• Confirm that data have been entered into all boxes in the latest version of record template, and that the data have been rigorously compared with the acceptance criteria.
- Handling of direct printouts and true copies from electronic systems
• For systems such as balances, pH meters, and records from these, the person who generated the record should sign and date the original record, include, in the record format, information that ensures traceability, such as a sample ID and a batch number, and attach the original to the batch record.
• "True copies" of paper documents should be issued and controlled in accordance with the following procedures.
[1] Acquire the original document to be copied.
[2] Photocopy the original document so that no information will be lost.
[3] Confirm that the photocopy is authentic, and sign and date the photocopy as a true copy.
- Storage method for records
• Records should be stored for at least the periods specified by GMP requirements.
• Records should be stored in designated places with appropriate security and in a traceable condition.
• In order to ensure the integrity of the archived records, access to the archived records should be restricted, and records of access and return should be created.
• Store the records in a place where they can be protected from damage and fire.

## Slide 18: Key points of data integrity, for computerized systems (1)
• Check items related to data management throughout the data lifecycle to ensure data integrity of the computerized system.
- Qualification and validation of computerized systems
- Periodic system evaluation of computerized systems
No computerized system qualification, validation, or periodic system evaluation is performed.
• The computerized system is not sufficiently visualized, so you may overlook a problem in the system! In addition, unvalidated systems may have significant data integrity vulnerabilities!
• Failure to update the system may adversely affect data integrity!
Recommended practices
Inadvisable practices
Notes: < Recommended actions >
(Confirmation to be done to ensure data integrity of computerized systems)
- Qualification and validation
• Validate the computerized system according to the following procedures.
[1] Create an inventory of computerized systems being used. (including name of system, installation location, function, evaluation of function and criticality of system and related data)
[2] Perform risk assessment for each system. Specify necessary controls methods, taking into account especially the principles of ALCOA +, to ensure data integrity.
[3] Prepare a validation report that includes at least the following items for each system.
- Confirmation of (1) environmental settings for critical systems and (2) methods of controlling restrictions on access to environmental settings and changes
- List of names and roles of all currently approved general users and all users with administrative authorization
- Audit trail and system log review frequency
[4] System qualification shall be performed prior to routine use. Qualification includes URS, FAT, SAT, IQ, OQ and PQ.
- Periodic system evaluation
• Periodically assess upgrade history, performance, and maintenance & inspection for data integrity controls. Include an assessment of impacts that changes may cause to data management and control of data integrity.

## Slide 19: Key points of data integrity, for computerized systems (2)
• Check items related to data management throughout the data lifecycle to ensure data integrity of the computerized system. (Continued)
- Assessment of data transfer between systems
- System security for computerized systems
Data transfer between computerized systems has not been evaluated.
• If there is any problem with the interface between systems, data may be lost or changed by mistake or fraudulently rewritten during the transfer process!
Login IDs and PWs for the computerized systems are shared among persons in charge.
• Anyone can modify and delete data!
• You cannot tell who performed the task!
Recommended practices
Inadvisable practices
Notes: < Recommended actions >
(Operations to be performed to ensure data integrity of computerized systems)
- Assessment of data transfer between systems
• Evaluate interfaces during validation, to ensure correct and complete transfer of data.
The interface should have an appropriate built-in checking function for proper and safe data entry and processing.
• Confirm that the readability of data (including existing stored data) is maintained throughout the life cycle.
- System security
• Establish and execute user access controls to prevent unauthorized access, alteration or deletion of data. For example:
[1] All users who need to access and use each system should be given an individual login ID and password.
To authorize system access for the first time, the user should create a new password according to the usual password rules.
[2] Data input to each system and changes to records should be made only by authorized personnel. The company should maintain and control a list of authorized personnel and access rights for each system.
• The following measures should be taken to prevent unauthorized changes to the validated system.
[1] Enhancement of physical security for system hardware
[2] Firewall settings to protect critical data and operations
• To ensure the authenticity and traceability of the persons who electronically sign records, properly control the electronic signatures used.
• From a system security perspective, the USB port should be disabled by default for client and server computers hosting GMP critical data.

## Slide 20: Key points of data integrity, for computerized systems (3)
• Check items related to data management throughout the data lifecycle to ensure data integrity of the computerized system. (Continued)
Audit trail for computerized systems
- Data acquisition and entry; data review; storage, archiving, and disposal of electronic data
Continuing to use an old computerized system without an electronic audit trail function
• Can you assure the data integrity? These kinds of systems are not able to keep the history of data change or deletion.
Manual analysis and reanalysis of test results have not been performed according to approved and controlled procedures.
• The data obtained may not be reliable because it cannot be guaranteed that the test results were processed in a correct manner!
Recommended practices
Inadvisable practices
Notes: < Recommended actions >
(Operations to be performed to ensure data integrity of computerized systems)
- System audit trail
• The audit trail should be enable reconstruction of the course of events related to creation, modification or deletion of electronic records.
In the absence of an electronic audit trail system, alternative methods of verifying control procedures, secondary checks, and control/data accuracy (e.g., recording data changes on paper) must be implemented.
• The audit trail function must always be enabled and must be set so that it cannot be disabled.
If an administrative user is able to disable the audit trail function, it is necessary to automatically enter, in the audit trail, data showing that the function has been disabled.
• Procedures describing the policy and process for review of audit trails should be prepared and implemented in accordance with the policy of risk management.
• Critical data should be reviewed with each record prior to final approval of the record.
• Ongoing review of audit trails should be incorporated into self-inspection program.
- Data collection/input (The system must be capable of properly collecting data whether by manual or automatic means of collection.)
• Essentials for manual entry
[1] Critical data should be input only by authorized persons, and the content of input, the person who performed the input, and date and time of input should be recorded in the system.
[2] Critical data entry should be verified by a secondary operator or a validated computer.
[3] Changes in input information must be captured by the audit trail and reviewed by an independent authorized person.
[4] Verify that invalid data forms are not accepted by the system.
• Essentials for automatic entry
[1] Validate the interface between the originating system, data collection system and recording system to ensure the accuracy of the data.
[2] Store the data collected by the system in memory that is difficult to manipulate, lose, or change.
[3] Incorporate a validated checking method into the system software to ensure the integrity of the acquired data and the meta data related to the data.
Required changes should be authorized and controlled according to approved procedures.
For example, if chromatography is to be reanalyzed, a written procedure should be prepared and followed, and each result should be stored as an object for review.
• Measures should be taken to ensure that data changes are made by designated personnel, only when necessary.
- Data Review
• The frequency of data review should be determined according to the value of data and the risk assessment.
• Procedures should be prepared describing methods of data review, inspection items, search methods, and procedures for actions to be taken when any problem is found in the review process.
For example, for critical data, it should be confirmed that operations are performed correctly and that there is no change (correction, deletion, overwriting) in original information of electronic records, or if there is, confirm formal permission.
• Data review is performed and approved by a designated competent person who has received appropriate training.
- Storage, archiving and disposal of electronic data
Data must be stored using a secure and validated process that includes all of the original data and metadata, including audit trails.
• Data will be archived periodically according to written procedures. Archived copies should be securely stored at a location separate from where the backup data and original data are stored.
• Data backup and copying should be controlled in the same manner, including protection against unauthorized access, data change or deletion, and falsification.
• Regularly test the procedure for restoring archived data. Specifically, maintain and make sure of an environment in which it is possible to access and review the stored data.
• Procedures should specify conditions for data disposition to ensure that the data required during the lifecycle are not accidentally disposed of.
• Electronic copies (of paper or electronic records) can be used as true copies if they maintain the content and meaning of the original data and contain relevant metadata and original records.

## Slide 21: Key points of data integrity, common to all types of records (1)
• Standard samples or other standard solutions are used in system suitability tests
• Personnel are trained to enable them to review and verify data integrity
Actual samples are used in system suitability testing, trial injection, and equilibration operations.
• It may be assumed that actual samples were used in trial injection and equilibration operations for the purpose of obtaining specific results (as a means of hiding inappropriate test results)!
Data are reviewed by personnel with inadequate training and experience in audit trails.
• The integrity of data reviewed as such may not be fully assured!
Recommended practices
Inadvisable practices
Notes: < Recommended actions >
(Activities to be performed to ensure data integrity)
- System suitability test precautions
• If actual samples are used for system suitability tests, the following must be ensured:
[1] The samples should be an appropriately identified secondary standard.
[2] The samples should be analyzed in accordance with the prepared procedure.
[3] The samples for SST should be from a batch different than that of the samples to be tested.
[4] All data should be stored, and the records should be reviewed.
- Personnel requirements
• Personnel should be trained to review data integrity as part of the routine GMP training program.

## Slide 22: Key points of data integrity, common to all types of records (2)
• Periodic risk reviews are performed for the supply chain, and necessary data integrity control measures are assessed.
• The scope of errors in data recording and reporting are comprehensively investigated.
Raw materials are purchased from manufacturers for whom no on-site audit has been performed.
• The data provided by the manufacturer may be unreliable because it has never been audited from the standpoint of data integrity!
GMP violations involving data integrity that were found during regulatory inspections were handled by personnel with limited knowledge of data integrity, who only addressed the findings themselves.
• Because the nature and root cause of data integrity failure cannot be completely extracted by such personnel, it may be difficult to plan improvement measures that are satisfactory to the regulatory authorities!
Recommended practices
Inadvisable practices
Notes: < Recommended actions >
(Activities to be performed to ensure data integrity)
- General supply chain data management
• Perform periodic risk reviews on the supply chain and external contractors, and assess necessary data integrity control measures.
Risk review includes review of on-site audit results and analytical data.
• Make quality agreements with CMOs to ensure data integrity.
- Handling of data integrity failures
• Comprehensively investigate the scope of errors in data recording and reporting.
[1] Conduct interviews with relevant personnel to determine the nature, scope and root cause of data errors.
[2] Find deficiencies at the facility, including neglect to evaluate the extent of data integrity failure, falsification, deletion, or disposal of data, and entry of non-contemporaneous records.
[3] Employment of a third-party consultant is recommended if it is confirmed that there is a potential violation of a comprehensive retrospective evaluation of the nature of the data integrity failure that is related to testing or manufacturing and its root cause.
In addition, it is recommended that individuals at all levels who are responsible for the problem be removed from GMP duties.
[4] Address data integrity vulnerabilities by developing corrective and preventive actions and a schedule for their implementation.
• Handle internal information on quality issues appropriately in accordance with a documented GMP quality system.

## Slide 23: Key points of data integrity, common to all types of records (3)
Changes in data
Are authorized and managed according to approved procedures.
The original data are retained in the original format.
All changes or corrections to original data are documented, and these are reviewed and approved by a designated competent person who has received appropriate training.
There is no procedure for entering, changing, correcting and reviewing important data.
If it is not known who entered what and when (Attributability), you cannot guarantee that it is the official data!
Data that are incorrectly entered may be approved as they are!
Data might be fraudulently changed!
=> Data falsification!
Recommended practices
Inadvisable practices
Notes: < Recommended actions >
(Activities to be performed to ensure data integrity)
When making changes in data, pay attention to the following points.
Necessary changes to data should be authorized and controlled according to approved procedures.
Take actions to ensure that data changes are made by a nominated person, only when necessary.
Retain the original (pre-change) data in the original format.
All changes or corrections to original data should be documented, and these should be reviewed and approved by a designated competent person who has received appropriate training.

## Slide 24: Table of Contents (Content for Working-Level Personnel)
Data Integrity - Why must we comply with this? –
What is ALCOA +?
Recommended practices / inadvisable practices
Examples of DI-related deviations (from FDA warning letters)
(Appendix) Glossary (from PIC/S DI guidance 13. Definitions)

## Slide 25: Warning letter example (1)
November 2017, German pharmaceutical company
Your firm failed to establish an adequate quality control unit with the responsibility and authority to approve or reject all components, drug product containers, closures, in-process materials, packaging materials, labeling, and drug products, and that approves or rejects all procedures or specifications impacting on the identity, strength, quality, and purity of the drug product (21 CFR 211.22(a) and (c)).
Observed discarded original personnel training records..
Observed discarded forms used to document and set inspection parameters for your automated tablet visual inspection machinery. These parameters are used to accept or reject tablets.
Your firm failed to ensure that laboratory records included complete data derived from all tests necessary to assure compliance with established specifications and standards (21 CFR 211.194(a)).
Observed unreported data from in-process tablet weight checks. You programmed your in-process weight checker not to report values that varied more than (b)(4)% from the tablet target weight.
Notes: The basis of GMP is to leave a record of what has been done.
It is necessary to leave records of training provided and retain the originals.
In addition, it is necessary (1) to keep records that show "how the testing equipment used in in-process control was confirmed to be operating properly," to ensure the quality of products, and (2) to prepare procedures for retaining such records.
To ensure the quality of the entire lot of product, it is not allowed that you selection and use only the portion of data that suits your purpose.

## Slide 26: Warning letter example (2)
HPLC chromatograms were deleted and not available for our investigators’ review
Found a recurring practice of re-testing samples until acceptable results were obtained.
The initial test result was invalidated. Only the results of the second analysis were used for batch disposition, without documented justification or investigation.
April 2017, Chinese pharmaceutical company
Failure to prevent unauthorized access or changes to data, and failure to provide adequate controls to prevent omission of data.
  Your analysts manipulated the date/time settings on your high performance liquid chromatography (HPLC) systems.
  Your analysts admitted to setting the clock back and repeating analyses for undocumented reasons.
  Initial sample results were overwritten or deleted, and unavailable for our investigators’ review.
  Your quality control analysts used a shared login account to access HPLC systems.
  This shared account allowed analysts, without traceability, to change the date/time settings of the computer, to modify file names, and to delete original HPLC data.
  your firm’s HPLC systems used for API testing had the audit trail feature disabled, although all (b)(4) had audit trail functionality.
Failure to maintain complete data derived from all laboratory tests conducted to ensure compliance with established specifications and standards.
Notes: The most common data integrity findings concern laboratory HPLC and GC.
HPLC and GC data are dynamic electronic records, and they should be stored as electronic raw data ensuring that they are original, attributable, complete and available.
For access to these laboratory instruments, ID and password should be granted to each individual, and shared use is not permitted. Users should be stratified into analysts, managers, and system administrators etc. to limit access to functions such as configuration changes, reanalysis, and deletion.
In addition, all data from the tests performed must be saved regardless of the results, and the audit trail must be checked periodically to ensure that there has been no unauthorized deletion or overwriting.
These electronic data should be backed up on a regular basis, archived in a secure location, and kept in a state in which results can be reproduced if necessary (available).

## Slide 27
October 2018, South Korean pharmaceutical company
Your firm failed to ensure that laboratory records included complete data derived from all tests necessary to assure compliance with established specifications and standards (21 CFR 211.194(a)).
Control of test records at QC laboratory was insufficient. Observed a quality control analyst and laboratory team leader signing and backdating a test record. Also observed an analyst recording microbiological test results from environmental monitoring settling plates before reading the plates.
Your firm failed to exercise appropriate controls over computer or related systems to assure that only authorized personnel institute changes in master production and control records, or other records (21 CFR 211.68(b)).
Three of your quality control team leaders had administrator privileges within your HPLC computerized laboratory software system. Because they review and approve CGMP data, their access level should preclude file deletion or modification.
In addition, two of your laboratory software systems had unlocked time and date functions, which allowed users to change the recorded dates and times of analyses.
Warning letter example (3)
Notes: This is a case where the contemporaneousness and accuracy of laboratory records are suspected.
What is required here, in addition to issuance control of test record forms, is a system like double-checking or photography that can guarantee the accuracy of records if these rely on visual inspection and do not contain electronic data, for example, the number of colonies on settle plates.
Operating authority must be stratified for analytical instruments that use computers, such as HPLC.
If QC equipment such as electronic balances has time and date setting functions and anyone can change them, data manipulation such as backdating may be suspected.

## Slide 28: Table of Contents (Content for Working-Level Personnel)
Data Integrity - Why must we comply with this? –
What is ALCOA +?
Recommended practices / inadvisable practices
Examples of DI-related deviations (from FDA warning letter)
(Appendix) Glossary (from PIC/S DI guidance 13. Definitions)

## Slide 29: What is Data Integrity?
Data integrity principles apply equally to paper, computerized and hybrid systems and should not limit the development or adoption of new concepts or technologies.
Good Documentation Practices (GDocPs) are the cornerstone of ensuring data integrity and are a fundamental part of a well-designed pharmaceutical quality system.
Management should be aware of legal and moral obligations (i.e., responsibilities and authorities) to prevent data integrity failures and detect them as they occur.
If a data integrity failure is found, it should be handled as a deviation based on the pharmaceutical quality system.
The extent to which all data are complete, consistent and accurate throughout the data lifecycle. Data should follow the principles of ALCOA +.

## Slide 30: What is data governance?
Data governance is the sum total of arrangements that provide assurance of data quality.
The data governance system should be integrated with the pharmaceutical quality system to ensure control according to the principles of quality risk management in the data lifecycle. (implementation of systems and procedures to minimize potential risks to data integrity)
The organizational arrangements for data governance should be documented and periodically reviewed within the pharmaceutical quality system.
An effective risk management approach to data governance takes into account the criticality and risk of the data.
The sum total of arrangements to ensure that data, irrespective of the format in which it is generated, is recorded, processed, retained and used to ensure a complete, consistent and accurate record throughout the data lifecycle.

## Slide 31: What are data?
Facts, figures and statistics collected together for reference or analysis.
What is the data lifecycle?
All phases in the life of the data (including raw data) from initial generation and recording through processing (including transformation or migration), use, data retention, archive / retrieval and destruction.

## Slide 32: What are meta data?
An audit trail is a type of meta data.
Data should include all of original data and meta data, including audit trails, and should be stored using a secure and validated process.
A complete record of electronically generated data should include relevant meta data.
An example of meta data): As a result (unit: mg) of from the weighing of sodium chloride of batch No. 1234 done by Mr. D.I. on ○/△/× (Month/Day/Year), a datum of "sodium chloride batch No. 1234, 3.5 mg, D.I. ○/△/×,“ is obtained; in this case, the results other than "3.5" are meta data.
Data that describes the attributes of other data, and provides context and meaning.

## Slide 33: What is an audit trail?
The company should endeavor to purchase and, thereafter, upgrade software containing an electronic audit trail function.
If the system does not have an audit trail function, other methods to verify the accuracy of the data should be implemented (e.g. control procedures, secondary checks).
The audit trail function should always be available and locked.
  Limit the audit trail function so that the user cannot modify it.
  If the audit trail function is disabled by the administrator, an entry indicating that the function is disabled is automatically entered in the audit trail.
Include the following parameters in the audit trail: Person making the change, details of the change (values before and after the change), date and time of the change, reason for the change, and name of approver.
It should be possible to print and provide an electronic copy of the audit trail.
GMP/GDP audit trails are metadata that are a record of GMP/GDP critical information (for example the change or deletion of GMP/GDP relevant data), which permit the reconstruction of GMP/GDP activities.

## Slide 34: What is an audit trail? (Continued)
Document (1) the degree of importance for each data and (2) operations done that need to be kept as audit trails.
It should be configured to record all manually initiated processes related to critical data.
Allow for the reconstruction of the course of events related to creation, modification or deletion of electronic records.
Procedures describing the audit trail review policy and process should be established in accordance with the risk management policy.
Review of audit trails should be performed periodically with review of data.
Critical audit trails for each operation should be reviewed independently of all other records related to the operation and be done prior to reviewing the completion of the operation (independently reviewed prior to batch release)
Review should be performed by the department in charge of preparation and verified by the quality unit if necessary.
GMP/GDP audit trails are metadata that are a record of GMP/GDP critical information (for example the change or deletion of GMP/GDP relevant data), which permit the reconstruction of GMP/GDP activities.

## Slide 35: What is archiving?
Obsolete master documents and files should be archived and access restricted.
Systems describing archiving steps are required. (identification of depository, list of records for each depository, storage periods, storage places, etc.)
Access to archived documents should be restricted to authorized personnel.
Store the data securely in a place separate from the storage place for backup data and original data.
Paper records: Store in an easily traceable and retrievable form in a secure location such that damage and loss are prevented and durability is ensured throughout the retention period. (Protection from fire, liquid, rodents, humidity, etc.)
Electronic records: Ensure that, when software is updated, archived data are readable by the new software. The records should be stored periodically according to the procedure. A restoration procedure is required.
Long-term, permanent retention of completed data and relevant meta data in its final form for the purposes of reconstruction of process or activity

## Slide 36: What is backup?
Backup should be subjected to an appropriate level of control, equivalent to that for the original data. (To prevent unauthorized access, data change or deletion, and falsification)
Maintain appropriate software and hardware to access backups.
Backups should be stored in a location physically separate from the original data.
A copy of current (editable) data, metadata and system configuration settings (e.g., variable settings which relate to an analytical run) maintained for the purpose of disaster recovery.